Safety data sheet

SECTION 1. Identification of the substance/mixture and of the company/undertaking

| 1.1. Product identifier |
| --- |
| Code: | 144029 |
| Product name | Light zinco |
| Chemical name and synonym | Protective Zinc |

| 1.2. Relevant identified uses of the substance or mixture and uses advised against |
| --- |
| Intended use | Zinc protective |

| 1.3. Details of the supplier of the safety data sheet |
| --- |
| Name | PINTURAS ISAVAL, S.L. |
| Full address | Calle Velluters, Parcela 2-14 – P.I. Casanova |
| District and Country | 46394 – Ribarroja del Turia (Valencia) |
|  | España |
|  | Tel. +34 96 1640001 |
|  | Fax +34 96 1640002 |
| e-mail address of the competent person |  |
| responsible for the Safety Data Sheet | atencionalcliente@isaval.es |

| 1.4. Emergency telephone number |
| --- |
| For urgent inquiries refer to | +34 96 1640001 (8:00 – 18:00 h) |

SECTION 2. Hazards identification.

2.1. Classification of the substance or mixture.

The product is classified as hazardous pursuant to the provisions set forth in EC Regulation 1272/2008 (CLP) (and subsequent amendments and supplements). The product thus requires a safety datasheet that complies with the provisions of EC Regulation 1907/2006 and subsequent amendments.

Any additional information concerning the risks for health and/or the environment are given in sections 11 and 12 of this sheet.

Hazard classification and indication:

| Aerosol, category 1 | H222 | Extremely flammable aerosol. |
| --- | --- | --- |
|  | H229 | Pressurised container: may burst if heated. |
| Aspiration hazard, category 1 | H304 | May be fatal if swallowed and enters airways. |
| Eye irritation, category 2 | H319 | Causes serious eye irritation. |
| Skin irritation, category 2 | H315 | Causes skin irritation. |
| Specific target organ toxicity - single exposure, category 3 | H336 | May cause drowsiness or dizziness. |
| Hazardous to the aquatic environment, acute toxicity, category 1 | H400 | Very toxic to aquatic life. |
| Hazardous to the aquatic environment, chronic toxicity, category 1 | H410 | Very toxic to aquatic life with long lasting effects. |

2.2. Label elements.

Hazard labelling pursuant to EC Regulation 1272/2008 (CLP) and subsequent amendments and supplements.

| Signal words: | Danger |
| --- | --- |

Hazard statements:

| H222 | Extremely flammable aerosol. |
| --- | --- |
| H229 | Pressurised container: may burst if heated. |
| H319 | Causes serious eye irritation. |
| H315 | Causes skin irritation. |
| H336 | May cause drowsiness or dizziness. |
| H410 | Very toxic to aquatic life with long lasting effects. |

Precautionary statements:

| P210 | Keep away from heat, hot surfaces, sparks, open flames and other ignition sources. No smoking. |
| --- | --- |
| P211 | Do not spray on an open flame or other ignition source. |
| P251 | Do not pierce or burn, even after use. |
| P264 | Wash . . . thoroughly after handling. |
| P280 | Wear protective gloves / eye protection / face protection. |
| P301+P310 | IF SWALLOWED: immediately call a POISON CENTER / doctor / . . . |
| P304+P340 | IF INHALED: remove person to fresh air and keep comfortable for breathing. |
| P410+P412 | Protect from sunlight. Do no expose to temperatures exceeding 50°C / 122°F. |
| Contains: | NAPHTHA (PETROLEUM), HYDROTREATED LIGHT |
|  | ACETONE |

| Statements on the aspiration toxicity classification were not included in the label elements, based on section 1.3.3. of Annex I to CLP. |  |
| --- | --- |

2.3. Other hazards.

On the basis of available data, the product does not contain any PBT or vPvB in percentage greater than 0,1%.

SECTION 3. Composition/information on ingredients.

3.1. Substances.

Information not relevant.

3.2. Mixtures.

Contains:

| Identification. | Conc. %. | Classification 1272/2008 (CLP). |  |
| --- | --- | --- | --- |
| BUTANE Reach 01-2119474691-32-0035 |  |  |  |
| CAS. 106-97-8 | 22,5 - 24 | Flam. Gas 1 H220, Note C U |  |
| EC. 203-448-7 |  |  |  |
| INDEX. 601-004-00-0 |  |  |  |
| PROPANE Reach 01-2119486944-21 |  |  |  |
| CAS. 74-98-6 | 22,5 - 24 | Flam. Gas 1 H220, Note U |  |
| EC. 200-827-9 |  |  |  |
| INDEX. 601-003-00-5 |  |  |  |
| NAPHTHA (PETROLEUM), HYDROTREATED LIGHT Reach 01-2119484651-34-XXXX |  |  |  |
| CAS. 64742-49-0 | 16,5 - 18 | Flam. Liq. 2 H225, Asp. Tox. 1 H304, Skin Irrit. 2 H315, STOT SE 3 H336, Aquatic Chronic 2 H411, Note P |  |
| EC. 265-151-9 |  |  |  |
| INDEX. 649-328-00-1 |  |  |  |
| Reg. no. 012119484561-34-xxxx |  |  |  |
| ACETONE Reach 01-2119471330-49 |  |  |  |
| CAS. 67-64-1 | 15 - 16,5 | Flam. Liq. 2 H225, Eye Irrit. 2 H319, STOT SE 3 H336, EUH066 |  |
| EC. 200-662-2 |  |  |  |
| INDEX. 606-001-00-8 |  |  |  |
| XYLENE (MIXTURE OF ISOMERS) Reach 01-2119488216-32-XXXX |  |  |  |
| CAS. 1330-20-7 | 8 - 9 | Flam. Liq. 3 H226, Acute Tox. 4 H312, Acute Tox. 4 H332, Skin Irrit. 2 H315, Note C |  |
| EC. 215-535-7 |  |  |  |
| INDEX. 601-022-00-9 |  |  |  |
| TALC – Reach 01-2119486866-17 |  |  |  |
| CAS. 14807-96-6 | 8 - 9 | Acute Tox. 4 H332, STOT SE 3 H335 |  |
| EC. 238-877-9 |  |  |  |
| INDEX. - |  |  |  |
| ZINC POWDER - ZINC DUST ( 100% - metallic element ) Reach 01-2119467174-37-0000 |  |  |  |
| CAS. 7440-66-6 | 7 - 8 | Aquatic Acute 1 H400 M=10, Aquatic Chronic 1 H410 M=10 |  |
| EC. 231-175-3 |  |  |  |
| INDEX. 030-001-01-9 |  |  |  |

Note: Upper limit is not included into the range.

The full wording of hazard (H) phrases is given in section 16 of the sheet.

SECTION 4. First aid measures.

4.1. Description of first aid measures.

EYES: Remove contact lenses, if present. Wash immediately with plenty of water for at least 15 minutes, opening the eyelids fully. If problem persists, seek medical advice.

SKIN: Remove contaminated clothing. Rinse skin with a shower immediately. Get medical advice/attention immediately. Wash contaminated clothing before using it again.

INHALATION: Remove to open air. If the subject stops breathing, administer artificial respiration. Get medical advice/attention immediately.

INGESTION: Get medical advice/attention immediately. Do not induce vomiting. Do not administer anything not explicitly authorised by a doctor.

4.2. Most important symptoms and effects, both acute and delayed.

For symptoms and effects caused by the contained substances, see chap. 11.

4.3. Indication of any immediate medical attention and special treatment needed.

Information not available.

SECTION 5. Firefighting measures.

5.1. Extinguishing media.

SUITABLE EXTINGUISHING EQUIPMENT

The extinguishing equipment should be of the conventional kind: carbon dioxide, foam, powder and water spray.

UNSUITABLE EXTINGUISHING EQUIPMENT

None in particular.

5.2. Special hazards arising from the substance or mixture.

HAZARDS CAUSED BY EXPOSURE IN THE EVENT OF FIRE

If overheated, aerosol cans can deform, explode and be propelled considerable distances. Put a protective helmet on before approaching the fire. Do not breathe combustion products.

5.3. Advice for firefighters.

GENERAL INFORMATION

Use jets of water to cool the containers to prevent product decomposition and the development of substances potentially hazardous for health. Always wear full fire prevention gear.

SPECIAL PROTECTIVE EQUIPMENT FOR FIRE-FIGHTERS

Normal fire fighting clothing i.e. fire kit (BS EN 469), gloves (BS EN 659) and boots (HO specification A29 and A30) in combination with self-contained open circuit positive pressure compressed air breathing apparatus (BS EN 137).

SECTION 6. Accidental release measures.

6.1. Personal precautions, protective equipment and emergency procedures.

Eliminate all sources of ignition (cigarettes, flames, sparks, etc.) from the leakage site. Send away individuals who are not suitably equipped. Wear protective gloves / protective clothing / eye protection / face protection.

6.2. Environmental precautions.

Do not disperse in the environment.

6.3. Methods and material for containment and cleaning up.

Use inert absorbent material to soak up leaked product. Make sure the leakage site is well aired. Contaminated material should be disposed of in compliance with the provisions set forth in point 13.

6.4. Reference to other sections.

Any information on personal protection and disposal is given in sections 8 and 13.

SECTION 7. Handling and storage.

7.1. Precautions for safe handling.

Avoid bunching of electrostatic charges. Do not spray on flames or incandescent bodies. Vapours may catch fire and an explosion may occur; vapour accumulation is therefore to be avoided by leaving windows and doors open and ensuring good cross ventilation. Do not eat, drink or smoke during use. Do not breathe spray.

7.2. Conditions for safe storage, including any incompatibilities.

Store in a place where adequate ventilation is ensured, away from direct sunlight at a temperature below 50°C/122°F, away from any combustion sources.

7.3. Specific end use(s).

Information not available.

SECTION 8. Exposure controls/personal protection.

8.1. Control parameters.

Regulatory References:

| DEU | Deutschland | MAK-und BAT-Werte-Liste 2012 |
| --- | --- | --- |
| ESP | España | INSHT - Límites de exposición profesional para agentes químicos en España 2015 |
| FRA | France | JORF n°0109 du 10 mai 2012 page 8773 texte n° 102 |
| GRB | United Kingdom | EH40/2005 Workplace exposure limits |
| ITA | Italia | Decreto Legislativo 9 Aprile 2008, n.81 |
| POL | Polska | ROZPORZĄDZENIE MINISTRA PRACY I POLITYKI SPOŁECZNEJ z dnia 16 grudnia 2011r |
| EU | OEL EU | Directive 2009/161/EU; Directive 2006/15/EC; Directive 2004/37/EC; Directive 2000/39/EC. |
|  | TLV-ACGIH | ACGIH 2014 |

| PROPANE |
| --- |
| Threshold Limit Value. |
| Type | Country | TWA/8h |  | STEL/15min |  |  |  |
|  |  | mg/m3 | ppm | mg/m3 | ppm |  |  |
| AGW | DEU | 1800 | 1000 | 7200 | 4000 |  |  |
| MAK | DEU | 1800 | 1000 | 7200 | 4000 |  |  |
| NDS | POL | 1800 |  |  |  |  |  |
| TLV-ACGIH |  |  | 1000 |  |  |  |  |

| BUTANE |
| --- |
| Threshold Limit Value. |
| Type | Country | TWA/8h |  | STEL/15min |  |  |  |
|  |  | mg/m3 | ppm | mg/m3 | ppm |  |  |
| AGW | DEU | 2400 | 1000 | 9600 | 4000 |  |  |
| MAK | DEU | 2400 | 1000 | 9600 | 4000 |  |  |
| VLA | ESP |  | 800 |  |  |  |  |
| VLEP | FRA | 1900 | 800 |  |  |  |  |
| WEL | GRB | 1450 | 600 | 1810 | 750 |  |  |
| NDS | POL | 1900 |  | 3000 |  |  |  |
| TLV-ACGIH |  |  |  | 2377 | 1000 |  |  |

| NAPHTHA (PETROLEUM), HYDROTREATED LIGHT |
| --- |
| Threshold Limit Value. |
| Type | Country | TWA/8h |  | STEL/15min |  |  |  |
|  |  | mg/m3 | ppm | mg/m3 | ppm |  |  |
| OEL | EU |  |  | 72 |  |  |  |
| Health - Derived no-effect level - DNEL / DMEL |
|  | Effects on consumers. |  |  |  | Effects on workers |  |  |  |
| Route of exposure | Acute local | Acute systemic | Chronic local | Chronic systemic | Acute local | Acute systemic | Chronic local | Chronic systemic |
| Oral. | 1301 mg/kg/d | 1301 mg/kg/d |  |  |  |  |  |  |
| Inhalation. |  |  | 1137 mg/m3 | 1137 mg/m3 |  |  | 5306 mg/m3 | 5306 mg/m3 |
| Skin. | 1377 mg/kg/d | 1377 mg/kg/d |  |  |  |  | 13964 mg/kg/d | 13964 mg/kg/d |

| ACETONE |
| --- |
| Threshold Limit Value. |
| Type | Country | TWA/8h |  | STEL/15min |  |  |  |
|  |  | mg/m3 | ppm | mg/m3 | ppm |  |  |
| AGW | DEU | 1200 | 500 | 2400 | 1000 |  |  |
| MAK | DEU | 1200 | 500 | 2400 | 1000 |  |  |
| VLA | ESP | 1210 | 500 |  |  |  |  |
| VLEP | FRA | 1210 | 500 | 2420 | 1000 |  |  |
| WEL | GRB | 1210 | 500 | 3620 | 1500 |  |  |
| TLV | ITA | 1210 | 500 |  |  |  |  |
| NDS | POL | 600 |  | 1800 |  |  |  |
| OEL | EU | 1210 | 500 |  |  |  |  |
| TLV-ACGIH |  | 1187 | 500 | 1781 | 750 |  |  |

| TALC |
| --- |
| Threshold Limit Value. |
| Type | Country | TWA/8h |  | STEL/15min |  |  |  |
|  |  | mg/m3 | ppm | mg/m3 | ppm |  |  |
| VLA | ESP | 2 |  |  |  |  |  |
| WEL | GRB | 1 |  |  |  |  |  |
| NDS | POL | 1 |  |  |  | RESP. |  |
| TLV-ACGIH |  | 2 |  |  |  |  |  |

| XYLENE (MIXTURE OF ISOMERS) |
| --- |
| Threshold Limit Value. |
| Type | Country | TWA/8h |  | STEL/15min |  |  |  |
|  |  | mg/m3 | ppm | mg/m3 | ppm |  |  |
| AGW | DEU | 440 | 100 | 880 | 200 | SKIN. |  |
| MAK | DEU | 440 | 100 | 880 | 200 | SKIN. |  |
| VLA | ESP | 221 | 50 | 442 | 100 | SKIN. |  |
| VLEP | FRA | 221 | 50 | 442 | 100 | SKIN. |  |
| WEL | GRB | 220 | 50 | 441 | 100 |  |  |
| TLV | ITA | 221 | 50 | 442 | 100 | SKIN. |  |
| NDS | POL | 100 |  |  |  |  |  |
| OEL | EU | 221 | 50 | 442 | 100 | SKIN. |  |
| TLV-ACGIH |  | 434 | 100 | 651 | 150 |  |  |

| ZINC POWDER - ZINC DUST |
| --- |
| Threshold Limit Value. |
| Type | Country | TWA/8h |  | STEL/15min |  |  |  |
|  |  | mg/m3 | ppm | mg/m3 | ppm |  |  |
| MAK | DEU | 0,1 |  | 0,4 |  | RESP. |  |

Legend:

(C) = CEILING   ;   INHAL = Inhalable Fraction   ;   RESP = Respirable Fraction   ;   THORA = Thoracic Fraction.

VND = hazard identified but no DNEL/PNEC available   ;   NEA = no exposure expected   ;   NPI = no hazard identified.

TLV of solvent mixture:      740 mg/m3.

8.2. Exposure controls.

As the use of adequate technical equipment must always take priority over personal protective equipment, make sure that the workplace is well aired through effective local aspiration. Personal protective equipment must be CE marked, showing that it complies with applicable standards.

Provide an emergency shower with face and eye wash station.

HAND PROTECTION

None required.

SKIN PROTECTION

Wear category II professional long-sleeved overalls and safety footwear (see Directive 89/686/EEC and standard EN ISO 20344). Wash body with soap and water after removing protective clothing.

EYE PROTECTION

Wear airtight protective goggles (see standard EN 166).

RESPIRATORY PROTECTION

If the threshold value (e.g. TLV-TWA) is exceeded for the substance or one of the substances present in the product, a mask with a type AX filter combined with a type P filter should be worn (see standard EN 14387).

Respiratory protection devices must be used if the technical measures adopted are not suitable for restricting the worker's exposure to the threshold values considered. The protection provided by masks is in any case limited.

ENVIRONMENTAL EXPOSURE CONTROLS.

The emissions generated by manufacturing processes, including those generated by ventilation equipment, should be checked to ensure compliance with environmental standards.

Product residues must not be indiscriminately disposed of with waste water or by dumping in waterways.

SECTION 9. Physical and chemical properties.

9.1. Information on basic physical and chemical properties.

| Appearance | aerosol |
| --- | --- |
| Colour | silver |
| Odour | characteristic of solvent |
| Odour threshold. | Not available. |
| pH. | Not available. |
| Melting point / freezing point. | Not available. |
| Initial boiling point. | < Not applicable. |
| Boiling range. | Not available. |
| Flash point. | < Not applicable. |
| Evaporation Rate | Not available. |
| Flammability of solids and gases | flammable gas |
| Lower inflammability limit. | Not available. |
| Upper inflammability limit. | Not available. |
| Lower explosive limit. | Not available. |
| Upper explosive limit. | Not available. |
| Vapour pressure. | Not available. |
| Vapour density | Not available. |
| Relative density. | Not available. |
| Solubility | insoluble |
| Partition coefficient: n-octanol/water | Not available. |
| Auto-ignition temperature. | Not available. |
| Decomposition temperature. | Not available. |
| Viscosity | Not available. |
| Explosive properties | Not available. |
| Oxidising properties | Not available. |

9.2. Other information.

| Solid content. | 15,00 % |
| --- | --- |
| VOC (Directive 2010/75/EC) : | 85,00 % |
| VOC (volatile carbon) : | 67,75 % |

SECTION 10. Stability and reactivity.

10.1. Reactivity.

There are no particular risks of reaction with other substances in normal conditions of use.

ACETONE: decomposes under the effect of heat.

10.2. Chemical stability.

The product is stable in normal conditions of use and storage.

10.3. Possibility of hazardous reactions.

No hazardous reactions are foreseeable in normal conditions of use and storage.

ZINC POWDER - ZINC DUST: risk of explosion on contact with: ammonium nitrate, ammonium sulphide, barium peroxide, lead nitride, chlorates, chromium trioxide, sodium hydroxide solutions, oxidising agents, performic acid, acids, tetrachloromethane, water. May react dangerously with alkali hydroxides, bromine pentafluoride, calcium chloride solution, fluorine, hexachloroethane, nitrobenzene, potassium dioxide, carbon disulphide, silver. Reacts with acids and strong alkalis developing hydrogen.

XYLENE (MIXTURE OF ISOMERS): stable, but may develop violent reactions in the presence of strong oxidising agents such as sulphuric and nitric acids and perchlorates. May form explosive mixtures with the air.

ACETONE: risk of explosion on contact with: bromine trifluoride, difluoro dioxide, hydrogen peroxide, nitrosyl chloride, 2-methyl-1,3 butadiene, nitromethane, nitrosyl perchlorate. Can react dangerously with: potassium tert-butoxide, alkaline hydroxides, bromine, bromoform, isoprene, sodium, sulphur dioxide, chromium trioxide, chromyl chloride, nitric acid, chloroform, peroxymonosulphuric acid, phosphoryl chloride, chromosulphuric acid, fluorine, strong oxidising agents. Develops flammable gases with nitrosyl perchlorate.

10.4. Conditions to avoid.

Avoid overheating.

ACETONE: avoid exposure to sources of heat and naked flames.

10.5. Incompatible materials.

Strong reducing or oxidising agents, strong acids or alkalis, hot material.

ZINC POWDER - ZINC DUST: water, strong alkalis and acids.

ACETONE: acid and oxidising substances.

10.6. Hazardous decomposition products.

ACETONE: ketenes and other irritating compounds.

SECTION 11. Toxicological information.

11.1. Information on toxicological effects.

In the absence of experimental data for the product itself, health hazards are evaluated according to the properties of the substances it contains, using the criteria specified in the applicable regulation for classification.It is therefore necessary to take into account the concentration of the individual hazardous substances indicated in section 3, to evaluate the toxicological effects of exposure to the product.

The introduction of even small quantities of this liquid into the respiratory system in case of ingestion or vomit may cause bronchopneumonia and pulmonary edema.

Acute effects: stinging eyes. Symptoms may include: rubescence, edema, pain and lachrymation. Ingestion may cause health problems, including stomach pain and sting, nausea and sickness.

Acute effects: contact with skin may cause: irritation, erythema, edema, dryness and chapped skin. Ingestion may cause health disorders, including stomach pain and sting, nausea and sickness.

This product contains highly volatile substances, which may cause serious depression of the central nervous system (CNS) and have negative effects, such as drowsiness, dizziness, slow reflexes, narcosis.

XYLENE (MIXTURE OF ISOMERS): has a toxic effect on the CNS (encephalopathies). Irritating to the skin, conjunctivae, cornea and respiratory apparatus.

XYLENE (MIXTURE OF ISOMERS)

LD50 (Oral).3523 mg/kg Rat

LD50 (Dermal).4350 mg/kg Rabbit

LC50 (Inhalation).26 mg/l/4h Rat

SECTION 12. Ecological information.

This product is dangerous for the environment and highly toxic for aquatic organisms. In the long term, it have negative effects on aquatic environment.

12.1. Toxicity.

| ZINC POWDER - ZINC DUST |  |  |
| --- | --- | --- |
| LC50 - for Fish. |  | 7,1 mg/l/96h Nothobranchius guentheri |
| EC50 - for Crustacea. |  | 2,8 mg/l/48h Daphnia magna |
| EC50 - for Algae / Aquatic Plants. |  | 0,015 mg/l/72h Pseudokirchneriella subcapitata |

12.2. Persistence and degradability.

| ZINC POWDER - ZINC DUST |  |  |
| --- | --- | --- |
| Solubility in water. |  | mg/l 0,1 - 100 |

Biodegradability: Information not available.

| XYLENE (MIXTURE OF ISOMERS) |  |  |
| --- | --- | --- |
| Solubility in water. |  | mg/l 100 - 1000 |

Biodegradability: Information not available.

| TALC |  |  |
| --- | --- | --- |
| Solubility in water. |  | < 0,1 mg/l |

| BUTANE |  |  |
| --- | --- | --- |
| Solubility in water. |  | mg/l 0,1 - 100 |

Rapidly biodegradable.

| PROPANE |  |  |
| --- | --- | --- |
| Solubility in water. |  | mg/l 0,1 - 100 |

Rapidly biodegradable.

| ACETONE |  |  |
| --- | --- | --- |

Rapidly biodegradable.

| NAPHTHA (PETROLEUM), HYDROTREATED LIGHT |  |  |
| --- | --- | --- |

Rapidly biodegradable.

12.3. Bioaccumulative potential.

| XYLENE (MIXTURE OF ISOMERS) |  |  |
| --- | --- | --- |
| Partition coefficient: n-octanol/water. |  | 3,12 |
| BCF. |  | 25,9 |

| BUTANE |  |  |
| --- | --- | --- |
| Partition coefficient: n-octanol/water. |  | 1,09 |

| PROPANE |  |  |
| --- | --- | --- |
| Partition coefficient: n-octanol/water. |  | 1,09 |

| ACETONE |  |  |
| --- | --- | --- |
| Partition coefficient: n-octanol/water. |  | -0,23 |
| BCF. |  | 3 |

12.4. Mobility in soil.

| XYLENE (MIXTURE OF ISOMERS) |  |  |
| --- | --- | --- |
| Partition coefficient: soil/water. |  | 2,73 |

| NAPHTHA (PETROLEUM), HYDROTREATED LIGHT |  |  |
| --- | --- | --- |
| Partition coefficient: soil/water. |  | 1,78 |

12.5. Results of PBT and vPvB assessment.

On the basis of available data, the product does not contain any PBT or vPvB in percentage greater than 0,1%.

12.6. Other adverse effects.

Information not available.

SECTION 13. Disposal considerations.

13.1. Waste treatment methods.

Reuse, when possible. Product residues should be considered special hazardous waste. The hazard level of waste containing this product should be evaluated according to applicable regulations.

Disposal must be performed through an authorised waste management firm, in compliance with national and local regulations.

Waste transportation may be subject to ADR restrictions.

CONTAMINATED PACKAGING

Contaminated packaging must be recovered or disposed of in compliance with national waste management regulations.

SECTION 14. Transport information.

14.1. UN number.

| ADR / RID, IMDG, IATA: | 1950 |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |

14.2. UN proper shipping name.

| ADR / RID: | AEROSOLS, FLAMMABLE |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| IMDG: | AEROSOLS (NAPHTHA (PETROLEUM), HYDROTREATED LIGHT) |  |  |  |  |  |
| IATA: | AEROSOLS, FLAMMABLE |  |  |  |  |  |

14.3. Transport hazard class(es).

| ADR / RID: | Class: 2 | Label: 2.1 |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| IMDG: | Class: 2 | Label: 2.1 |  |  |  |  |
| IATA: | Class: 2 | Label: 2.1 |  |  |  |  |

14.4. Packing group.

| ADR / RID, IMDG, IATA: | - |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |

14.5. Environmental hazards.

| ADR / RID: | Environmentally Hazardous. |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| IMDG: | Marine Pollutant. |  |  |  |  |  |
| IATA: | NO |  |  |  |  |  |

For Air transport, environmentally hazardous mark is only mandatory for UN 3077 and UN 3082.

14.6. Special precautions for user.

| ADR / RID: |  | HIN - Kemler: -- |  | Limited Quantities: 1 L |  | Tunnel restriction code: (D) |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | Special Provision: - |  |  |  |  |
| IMDG: |  | EMS: F-D, S-U |  | Limited Quantities: 1 L |  |  |
| IATA: |  | Cargo: |  | Maximum quantity: 150 Kg |  | Packaging instructions: 203 |
|  |  | Pass.: |  | Maximum quantity: 75 Kg |  | Packaging instructions: 203 |
|  |  | Special Instructions: |  | A145, A167, A802 |  |  |

14.7. Transport in bulk according to Annex II of MARPOL73/78 and the IBC Code.

Information not relevant.

SECTION 15. Regulatory information.

15.1. Safety, health and environmental regulations/legislation specific for the substance or mixture.

| Seveso category. | 8, 9i |
| --- | --- |

Restrictions relating to the product or contained substances pursuant to Annex XVII to EC Regulation 1907/2006.

Product.

| Point. | 40 |  |
| --- | --- | --- |

Substances in Candidate List (Art. 59 REACH).

None.

Substances subject to authorisarion (Annex XIV REACH).

None.

Substances subject to exportation reporting pursuant to (EC) Reg. 649/2012:

None.

Substances subject to the Rotterdam Convention:

None.

Substances subject to the Stockholm Convention:

None.

Healthcare controls.

Workers exposed to this chemical agent must not undergo health checks, provided that available risk-assessment data prove that the risks related to the workers' health and safety are modest and that the 98/24/EC directive is respected.

15.2. Chemical safety assessment.

No chemical safety assessment has been processed for the mixture and the substances it contains.

SECTION 16. Other information.

Text of hazard (H) indications mentioned in section 2-3 of the sheet:

| Flam. Gas 1 | Flammable gas, category 1 |  |
| --- | --- | --- |
| Aerosol 1 | Aerosol, category 1 |  |
| Aerosol 3 | Aerosol, category 3 |  |
| Flam. Liq. 2 | Flammable liquid, category 2 |  |
| Flam. Liq. 3 | Flammable liquid, category 3 |  |
| Acute Tox. 4 | Acute toxicity, category 4 |  |
| Asp. Tox. 1 | Aspiration hazard, category 1 |  |
| Eye Irrit. 2 | Eye irritation, category 2 |  |
| Skin Irrit. 2 | Skin irritation, category 2 |  |
| STOT SE 3 | Specific target organ toxicity - single exposure, category 3 |  |
| Aquatic Acute 1 | Hazardous to the aquatic environment, acute toxicity, category 1 |  |
| Aquatic Chronic 1 | Hazardous to the aquatic environment, chronic toxicity, category 1 |  |
| Aquatic Chronic 2 | Hazardous to the aquatic environment, chronic toxicity, category 2 |  |
| H220 | Extremely flammable gas. |  |
| H222 | Extremely flammable aerosol. |  |
| H229 | Pressurised container: may burst if heated. |  |
| H225 | Highly flammable liquid and vapour. |  |
| H226 | Flammable liquid and vapour. |  |
| H312 | Harmful in contact with skin. |  |
| H332 | Harmful if inhaled. |  |
| H304 | May be fatal if swallowed and enters airways. |  |
| H319 | Causes serious eye irritation. |  |
| H315 | Causes skin irritation. |  |
| H335 | May cause respiratory irritation. |  |
| H336 | May cause drowsiness or dizziness. |  |
| H400 | Very toxic to aquatic life. |  |
| H410 | Very toxic to aquatic life with long lasting effects. |  |
| H411 | Toxic to aquatic life with long lasting effects. |  |
| EUH066 | Repeated exposure may cause skin dryness or cracking. |  |

LEGEND:

- ADR: European Agreement concerning the carriage of Dangerous goods by Road

- CAS NUMBER: Chemical Abstract Service Number

- CE50: Effective concentration (required to induce a 50% effect)

- CE NUMBER: Identifier in ESIS (European archive of existing substances)

- CLP: EC Regulation 1272/2008

- DNEL: Derived No Effect Level

- EmS: Emergency Schedule

- GHS: Globally Harmonized System of classification and labeling of chemicals

- IATA DGR: International Air Transport Association Dangerous Goods Regulation

- IC50: Immobilization Concentration 50%

- IMDG: International Maritime Code for dangerous goods

- IMO: International Maritime Organization

- INDEX NUMBER: Identifier in Annex VI of CLP

- LC50: Lethal Concentration 50%

- LD50: Lethal dose 50%

- OEL: Occupational Exposure Level

- PBT: Persistent bioaccumulative and toxic as REACH Regulation

- PEC: Predicted environmental Concentration

- PEL: Predicted exposure level

- PNEC: Predicted no effect concentration

- REACH: EC Regulation 1907/2006

- RID: Regulation concerning the international transport of dangerous goods by train

- TLV: Threshold Limit Value

- TLV CEILING: Concentration that should not be exceeded during any time of occupational exposure.

- TWA STEL: Short-term exposure limit

- TWA: Time-weighted average exposure limit

- VOC: Volatile organic Compounds

- vPvB: Very Persistent and very Bioaccumulative as for REACH Regulation

- WGK: Water hazard classes (German).

GENERAL BIBLIOGRAPHY

1. Regulation (EU) 1907/2006 (REACH) of the European Parliament

2. Regulation (EU) 1272/2008 (CLP) of the European Parliament

3. Regulation (EU) 790/2009 (I Atp. CLP) of the European Parliament

4. Regulation (EU) 2015/830 of the European Parliament

5. Regulation (EU) 286/2011 (II Atp. CLP) of the European Parliament

6. Regulation (EU) 618/2012 (III Atp. CLP) of the European Parliament

7. Regulation (EU) 487/2013 (IV Atp. CLP) of the European Parliament

8. Regulation (EU) 944/2013 (V Atp. CLP) of the European Parliament

9. Regulation (EU) 605/2014 (VI Atp. CLP) of the European Parliament

- The Merck Index. - 10th Edition

- Handling Chemical Safety

- INRS - Fiche Toxicologique (toxicological sheet)

- Patty - Industrial Hygiene and Toxicology

- N.I. Sax - Dangerous properties of Industrial Materials-7, 1989 Edition

- ECHA website

Note for users:

The information contained in the present sheet are based on our own knowledge on the date of the last version. Users must verify the suitability and thoroughness of provided information according to each specific use of the product.

This document must not be regarded as a guarantee on any specific product property.

The use of this product is not subject to our direct control; therefore, users must, under their own responsibility, comply with the current health and safety laws and regulations. The producer is relieved from any liability arising from improper uses.

Provide appointed staff with adequate training on how to use chemical products.

Changes to previous review:

The following sections were modified:

02 / 03 / 08 / 09 / 11 / 15 / 16.